## Slide 1: NASA GEOS-CF: Overview, Applications, Future Direction
K. Emma Knowland
Co-author: Christoph Keller1,2, Viral Shah2,3, Pam Wales1,2, Kris Wargan2,3, Brad Weir1,2, Lesley Ott2, Steven Pawson2
In collaboration with many other scientists from NASA Goddard Space Flight Center and our partners
1 Morgan State University/GESTAR-II
2 NASA Global Modeling and Assimilation Office (GMAO)
3 Science Systems and Applications, Inc. (SSAI)
27 October 2023

## Slide 2: GEOS-CF produces daily global forecasts of atmospheric composition at 0.25° resolution
GEOS NWP
GEOS - Chem
Keller, C. A., Knowland, K. E., et al. (2021). Description of the NASA GEOS composition forecast modeling system GEOS-CF v1.0. Journal of Advances in Modeling Earth Systems (JAMES), 13, e2020MS002413. https://doi.org/10.1029/2020MS002413
Knowland, K. E., Keller, C. A., et al. (2022). NASA GEOS Composition Forecast Modeling System GEOS‐CF v1.0: Stratospheric Composition. JAMES https://doi.org/10.1029/2021MS002852
Knowland, K. E., Keller, C. A., and Lucchesi, R. 2022. "File Specification for GEOS-CF Products." GMAO Office Note No. 17 (Version 1.3), available from http://gmao.gsfc.nasa.gov/pubs/office_notes
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov
Ozone (O3)
Nitrogen Dioxide (NO2)
Fine Particulate Matter (PM2.5)

## Slide 3: GEOS-CF v1 Status
Daily GEOS-CF global 5-day composition forecasts at 0.25° (25km) resolution are generated in near-real time:
  High-resolution historical estimates for fields are available since January 2018
  Forecast visualizations and links to data available at fluid.nccs.nasa.gov/cf and /cf_map
Applications include:
  NASA field missions (e.g., SCOAPE, FIREX-AQ, ACT-America, TRACER-AQ)
  Daily alerts sent to NASA TOLNet lidar teams (Matt Johnson, NASA Ames)
  TEMPO a priori for trace gas retrieval
  Cloud platforms, e.g., Google Earth Engine, WRI Resource Watch, CDC Tracker
Keller, C. A., et al. (2021). Description of the NASA GEOS composition forecast modeling system GEOS-CF v1.0. Journal of Advances in Modeling Earth Systems, 13, e2020MS002413. https://doi.org/10.1029/2020MS002413
Knowland, K. E., et al. (2022). NASA GEOS Composition Forecast Modeling System GEOS‐CF v1.0: Stratospheric Composition. JAMES https://doi.org/10.1029/2021MS002852
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov
Notes:   Running with full chemistry for the entire GEOS atmosphere (from the surface to the mesosphere) is very computationally expensive, so GEOS-CF is run once per day and separate from GEOS FP. After 2 weeks, our forecasts are archived; however the 5-day forecasts of the model’s “surface” concentrations of the five most-requested pollutants (PM2.5, O3, NO2, SO2, and CO) are available since January 2019. The first version of GEOS-CF ran for many years without more than a couple bug fixes so that we could thoroughly understand the system and two papers were published led by Christoph and myself on the GEOS-CF modeling system and both tropospheric and stratospheric composition.
  I’ll next go through some of the examples of the applications, our reason to push our system to be state-of-the-science.

## Slide 4
Realistic tropospheric and stratospheric composition is critical for many NASA applications
Realistic troposphere and stratosphere in GEOS-CF are essential to support a broad range of NASA applications, including:
  Satellite retrievals of trace gases
  Airborne campaigns
  Stratosphere-troposphere exchange
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov
Notes: It is important to note that the NASA GMAO products are designed to be research products and support many different NASA activities – which measure throughout the full atmosphere, therefore GEOS-CF is not optimized for capturing surface air quality. The GEOS-CF replay and forecasts can be used to support ground-based, balloon, and satellite-based instrument teams, as well as field and aircraft campaigns, which measure trace gases in the troposphere and the stratosphere.
The upcoming TEMPO geostationary satellite designed to monitor pollution over much of North America is to be launched in spring 2023 and we are working with the retrieval team to use GEOS-CF as their prior for trace gas retrievals.
For surface air quality, it is also important that the GEOS-CF simulates the stratosphere to troposphere transport correctly as these layers have very different chemical and meteorological conditions. We work with two ground-based instrument networks which observe ozone, the PANDORA instruments, which can also measure other species, and the Tropospheric ozone LIDAR Network, TOLNET.

## Slide 5: TEMPO specific collection: “sat_inst_1hr_r721x361_v72”
Regional Chemistry and Meteorology Diagnostics to support TEMPO satellite
Frequency: hourly instantaneous from 00:00 UTC
Spatial Grid: 3D, model-level, subset region of full horizontal resolution
Dimensions: longitude=721, latitude=361, every 0.25º
longitude: 0º to -180º
latitude: 0º to 90º
vertical level: 72 layers
Granule Size: ~258 MB per file
Start date: 00 UTC 1 January 2022
Mode: Replay only; Forecasts available based on mission requirements
Knowland et al., 2022. "File Specification for GEOS-CF Products." GMAO Office Note No. 17 (Version 1.3), available from http://gmao.gsfc.nasa.gov/pubs/office_notes
Name | Dim | Description | Units
BrO | tzyx | Bromine monoxide (BrO, MW = 96.00 g mol-1) volume mixing ratio dry air | mol mol-1
FRSEAICE | tyx | ice covered fraction of tile | 1
FRSNO | tyx | fractional area of land snowcover | 1
GLYX | tzyx | Glyoxal (CHOCHO, MW = 58.00 g mol-1) volume mixing ratio dry air | mol mol-1
HCHO | tzyx | Formaldehyde (CH2O, MW = 30.00 g mol-1) volume mixing ratio dry air | mol mol-1
HNO2 | tzyx | Nitrous acid (HNO2, MW = 47.00 g mol-1) volume mixing ratio dry air | mol mol-1
IO | tzyx | Iodine monoxide (IO, MW = 143.00 g mol-1) volume mixing ratio dry air | mol mol-1
NO2 | tzyx | Nitrogen dioxide (NO2, MW = 46.00 g mol-1) volume mixing ratio dry air | mol mol-1
O3 | tzyx | Ozone (O3, MW = 48.00 g mol-1) volume mixing ratio dry air | mol mol-1
OClO | tzyx | Chlorine dioxide (OClO, MW = 67.00 g mol-1) volume mixing ratio dry air | mol mol-1
PHIS | tyx | surface geopotential height | m+2 s-2
PS | tyx | surface pressure | Pa
Q | tzyx | specific humidity | kg kg-1
SNODP | tyx | snow depth | m
SNOMAS | tyx | Total snow storage land | kg m-2
SO2 | tzyx | Sulfur dioxide (SO2, MW = 64.00 g mol-1) volume mixing ratio dry air | mol mol-1
T | tzyx | air temperature | K
TROPPB | tyx | tropopause pressure based on blended estimate | Pa
U2M | tyx | 2-meter eastward wind | m s-1
V2M | tyx | 2-meter northward wind | m s-1
ZPBL | tyx | planetary boundary layer height | m
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov

## Slide 6: GEOS-CF with stratospheric chemistry adds near-real-time stratospheric ozone forecasting capability to the NASA GMAO
Ozonewatch.gsfc.nasa.gov
Average Column Ozone (DU)
NH Polar Cap
5 March 2020 Forecast
5-Days
HCl
Ozone
ClO
March 10, 2020
Ozonewatch
March 5, 2020
GEOS-CF
Knowland et al., JAMES, 2022, https://doi.org/10.1029/2021MS002852
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov

## Slide 7: Spinning up GEOS-CF version 2
Model update to GEOS-Chem v14.0
GEOS AGCM update
CEDS emission inventory (latest release through 2019)
Constituent Data Assimilation System (CoDAS)
  Multi-constituent assimilation with O3, NO2, SO2
Output will include simulated CO2 and CH4 (GOCART)
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov
Notes: Simulated CO2 and CH4 obtained from GEOS-GHG project forward.

## Slide 8
Designed to be tracer agnostic: can assimilate any type of retrieved constituent observations with an averaging kernel or at a point
  CoDAS builds on the Gridpoint Statistical Interpolation scheme developed at NCEP and GMAO
Constituent Data Assimilation System (CoDAS)
M2-SCREAM
Wargan et al., ESS (2023).
DOI: 10.1029/2022EA002632
Weir et al., Sci. Adv. (2021) DOI:10.1126/sciadv.abf9415
https://gmao.gsfc.nasa.gov/research/science_snapshots/2022/mauna-loa.php
GEOS-GHG
GEOS-CF v2
GMAO involved and invested in the constituent DA with JEDI
8
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov

## Slide 9: SO2 assimilation: Mauna Loa’s smoking gun
Simulated SO2 total column [DU] for Dec 6, 2022
Mauna Loa eruption only captured in runs with assimilation
Evolution of assimilated SO2 from the Mauna Loa eruption in November 2022
The resulting volcanic plume of sulfur dioxide (SO2) can be seen from space with satellite instruments such as NASA’s Ozone Monitoring Instrument (OMI).
https://gmao.gsfc.nasa.gov/research/science_snapshots/2022/mauna-loa.php
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov
Notes: Hawaii’s Mauna Loa began erupting on Nov. 27, 2022. The resulting volcanic plume of sulfur dioxide (SO2) can be seen from space with satellite instruments such as NASA’s Ozone Monitoring Instrument (OMI). Combining these observations with atmospheric models such as GEOS provides a powerful tool to simulate and predict the nature of these plumes in near real-time. Experiments using the GEOS model highlight the value of actively assimilating OMI SO2 into the model in order to realistically capture active volcanic plumes. Without assimilation (control run), the model solely relies on historical estimates of persistent degassing, missing the large release of SO2 from Mauna Loa’s eruption. On the other hand, the assimilation experiment adds SO2 over the source region, as informed by OMI. Once released, the SO2 gets lifted and dispersed eastward by the atmospheric winds. The capability to assimilate tropospheric trace gases is the latest extension of GMAO’s constituent assimilation system. This feature will be included in future GMAO products.

## Slide 10: NO2 assimilation ➡️ Improved NO2 in polluted areas
Global
Polluted areas
Increments smaller than O-F’s – reflects the ratio of observation to background errors
A slight high bias in the background
(column > 6 DU)
Mostly
Strat NO2 in remote atmosphere
Frequency distributions of O-F and O-A
Assimilating OMI NO2 total slant columns
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov
Notes: Assimilating total slant columns
1-month test run at c90 resolution (results for 2018-07-15)
Overall improvements are small (lifetime, 3Dvar, overpass time). It’s hard to see improvement in the system because of how system is designed.

## Slide 11: Ozone assimilation ➡️ Improved tropospheric ozone
Ozone assimilation of MLS v4.2 profiles, Total Column Ozone from OMI, and 9.6-micron radiances drastically improves the representation of ozone in the remote atmosphere according to this comparison to ATom-4 measurements and a version of the GEOS-CF v2 system used in testing.
Figure reproduced from Makoto M Kelp et al 2023 Environ. Res. Lett. 18 094036 DOI 10.1088/1748-9326/acf0b7
11
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov

## Slide 12
GEOS-CF v2 updates (including DA) positively impact O3 and PM2.5
New Meteorology ➡️ Improved summertime (JJA) surface O3
GEOS-CF v1 uses HTAP v2.2 which is now >10 years behind
Using latest CEDS with current estimates ➡️ Improved annual PM2.5
Ozone assimilation ➡️ Improved tropospheric ozone
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov
Notes: O3 sfc jja, pm annual mean

## Slide 13: Lines of development and legacy systems
GEOS CR development
MERRA-2 Stratospheric Composition Reanalysis with Aura MLS
(M2-SCREAM)
Greenhouse Gas data assimilation (GEOS-GHG)
Air quality / tropospheric chemistry modeling and assimilation
M2-SCREAM pathfinder for composition reanalysis with coupled chemistry model and multi-constituent data assimilation
GEOS-CF v2 near-real time system with multi-constituent data assimilation of (mainly) tropospheric constituents
GEOS Composition Reanalysis for the 21st Century
Assimilation of chemically reactive carbon species: CO2 and CH4
13
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov

## Slide 14: GEOS Composition Reanalysis of the 21st Century System Design
Assimilation of selected gases important for stratospheric and tropospheric chemistry, with CoDAS
Model: GEOS AGCM with the GEOS-Chem full chemistry model and a carbon module (developed from legacy GOCART)
  Coupling GEOS-Chem to GOCART aerosols under development
Constrained by temperature, winds, surface pressure, tropospheric water vapor from a GMAO reanalysis (“meteorological replay” technique)
14
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov

## Slide 15
Detrended anomalies in constituent fields from M2-SCREAM
Our surprising stratosphere
A series of large stratospheric perturbations occurred in the last five years.
Continuing measurements of the stratosphere will be essential for reanalyses.
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov

## Slide 16: Assimilated species and sensors
Sensor | Molecules | Observation type
OMI, TROPOMI, OMPS | NO2, SO2, O3 | Column
SCIAMACHY, GOSAT, TROPOMI | CH4 | Column
SCIAMACHY, GOSAT, OCO | CO2 | Column
MOPITT TIR & NIR | CO | Column
MLS | O3, HCl, HNO3, N2O, H2O, CH3Cl, CO | Stratospheric limb profiles
OMPS-LP | O3 | Stratospheric limb profiles
Retrievals
Radiances
Sensor | Wavelength | Comment
AIRS, IASI (MetOp-A,B), CrIS FSR (potentially) | 9.6 μm | Ozone-sensitive channels
established new
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov
16

## Slide 17: Preparing for the end of EOS missions
The assimilation of SAGE water vapor is now possible in the GEOS CoDAS framework to carry-on the trend and climate assessments after the Aura mission.
There is a clear benefit to assimilating the less frequent SAGE III/ISS water vapor observations, especially after anomalous events like the period following the Hunga Tonga Eruption.
https://gmao.gsfc.nasa.gov/weather_prediction/GEOS-CF/
k.e.knowland@nasa.gov
Tropical tape recorder signal assessed as anomalies in water vapor for 15°S to 15°N. Figure from Knowland et al. in prep
Notes: Assimilating water vapor only from the SAGE III occultation instrument onboard the ISS in a M2-SCREAM like system is able to represent similar stratospheric water vapor as an assimilation with MLS and compared well with independent observations from frost-point hygrometers and ACE-FTS.

## Slide 18: Summary
GMAO has a state-of-the-science Earth System model and data assimilation system
Daily GEOS-CF global 5-day composition forecasts at 0.25° (25km) resolution are generated in near-real time
GEOS-CF v2 will include CoDAS with O3, NO2, and SO2
GEOS Composition Reanalysis builds on the development of tropospheric and stratospheric composition modeling and assimilation at GMAO
Involved and invested in new data assimilation infrastructure for multi-constituent data assimilation system
NASA products are research products
Thank you for listening!
K. Emma Knowland k.e.knowland@nasa.gov
Notes: GMAO’s GEOS systems are central to NASA’s Earth Science Mission. They provide NASA’s platform for model-based mission support, research, and applications. They are key to many inter-agency collaborations.