## Slide 1: GEOS-5 River Routing Model

## Slide 2: Content
Global River Network
River Routing Model
Model Validation/Applications
  Observed streamflow data used
  Routing MERRA2 gridded runoff
  Routing SMAP L4 and SMAP Nature gridded runoff
  Flood events during the SMAP period
  Drought indices and teleconnections

## Slide 3: Global River Network
291,284 Pfafstetter Level 12 watersheds globally.
min_lon, max_lon, min_lat, max_lat, mean_elevation, area, length, ElevDiff, dnst_pfaf_index, DN_long, DN_lat, UP_lon, UP_lat, mouth_lon, and mouth_lat have been derived on each watershed.

## Slide 4: River Routing Model
WS
WR
QOUT to downstream watershed
QIN from upstream watersheds
total runoff from land model

## Slide 5
River Routing Model
Linear reservoir model :
Reservoir Coefficient for Wstream (Kstream):
Reservoir Coefficient
for Wriver (Kriver):
P1 = 0.010611
P2 = 0.188556
P3 = 0.096864
P4 = 0.691310
P5 = 0.365747
P6 = 0.009831
L = Area / length
If (Qrun < 2 ; K = K2) : a = P1; b = P2
If (Qrun > 10 ; K = K10): a = P3; b = P4
If (2 <= Qrun <= 10) : K = K2 + (Qrun -2)*(K10 – K2)/8.
L = length; a = P5; b = P6; where

## Slide 6: Model Validation/Applications
 | Daily Simulations |  | Monthly Simulations | 
 | US Floods in SMAP period (2015.04-2017.09) | 573 Unregulated basins in the US | Naturalized streamflows from 23 basins in the US (1980-2009) | 554 Global large river basins (1980-2009)
MERRA2 | Y | Y | Y | Y
SMAP L4 Vv3030 | Y | Y | N | N
SMAP Nature OL3001 | Y | Y | N | N

## Slide 7: Model Validation/Applications
Unregulated daily streamflow data (1980-2017) from 573 basins
Naturalized monthly streamflow data (1980-2009) from 23 basins
Monthly streamflow data (1980-2009) from 554 large basins

## Slide 8: Model Validation/Applications
TIME SERIES COMPARISON
Daily Simulations (1) : US Flood events in the SMAP period (2015.04-2017.09)
ftp://gmaoftp.gsfc.nasa.gov/pub/data/sarith/ROUTING_MODEL/smap_floods.pdf
SMAP Nature SMAP L4 MERRA2
Daily Simulations (2) : Model Validation on 573 basins for 2015.04 – 2017.09
ftp://gmaoftp.gsfc.nasa.gov/pub/data/sarith/ROUTING_MODEL/daily/SMAP-daily573.pdf
Observation SMAP L4 SMAP Nature MERRA2
Daily Simulations (3) : Model Validation on 573 basins for 1980 – 2017
ftp://gmaoftp.gsfc.nasa.gov/pub/data/sarith/ROUTING_MODEL/daily/M2-daily573.pdf
Observation MERRA2

## Slide 9: Model Validation/Applications
Skill of Daily Simulations : Correlation R (573 basins 2015 – 2017)
Daily streamflows from a 3-day moving window for the warm period April-Sep were used

## Slide 10: Model Validation/Applications
Skill of Daily Simulations : Nash-Sutcliffe Efficiency (573 basins 2015 – 2017)
Daily streamflows from a 3-day moving window for the warm period April-Sep were used

## Slide 11: Model Validation/Applications
Skill of Daily Simulations : Summary (573 basins 2015 – 2017)
Daily streamflows from a 3-day moving window for the warm period April-Sep were used

## Slide 12: Model Validation/Applications
Skill of Monthly Simulations : Correlation R of monthly streamflow anomalies (23 naturalized basins 1980 – 2009)

## Slide 13: Model Validation/Applications
Skill of Monthly Simulations : Correlation R of monthly streamflow anomalies (554 basins 1980 – 2009)

## Slide 14: Model Validation/Applications
Summary of Skill of Monthly Simulations : Correlation R of monthly streamflow anomalies (554 basins 1980 – 2009)

## Slide 15: Model Applications
  Drought indices and NAO teleconnection