File Specification for GEOS-DAS Gridded Output

Version 5.3

Global Modeling and Assimilation Office

Goddard Space Flight Center, Greenbelt, Maryland

http://gmao.gsfc.nasa.gov

Release Date March 30, 2004; Expiration Date March 30, 2009

Version 5.3

To support EOS with GEOS-4.x

Document maintained by Rob Lucchesi (GMAO, SAIC)

Permission to quote from this document should be obtained from the GMAO.

Michele Rienecker

Global Modeling and Assimilation Office

Earth Sciences Directorate

NASA Goddard Space Flight Center

Greenbelt, Maryland 20771

This page intentionally left blank.

File Specification for GEOS-DAS Gridded Output

Document No. GMAO-1001v5.3

March 30, 2004

Approved by:

__________________________________	 		__________________________________

Michele Rienecker	Date			Gi-Kong Kim                                  Date

Head		 			CCB Chair

Global Modeling and Assimilation Office			Global Modeling and Assimilation Office

Code 900.3, NASA GSFC				Code 902.0, NASA GSFC

REVISION HISTORY

| Version Number | Revision Date | Pages Affected/Extent of Changes | Approval Authority |
| --- | --- | --- | --- |
| Version 1.0 (original - no electronic copy) | April 8, 1997 | All | Not Approved |
| Version 3.0 (DAO-1001v3.0) | November 4, 1997 | - Added 5 authors - Reorganized the document - Replaced Sections 3, 5, 6, and Appendix B | Not Approved |
| Version 3.1 (DAO-1001v3.1) | January 5, 1998 | - Added Figure 1 - Revised size estimate for single level mis and lsm in Sections 6.1 and 6.2 - Made various changes to the list of variables in the assimilated time averaged files in Section 6.3 | Rob Lucchesi 1/26/99 (Closed CR 131) |
| Version 3.2 (DAO-1001v3.2) | March 4, 1999 | - Changed "GEOS-3" to "GEOS-AM1" throughout the document - Updated scope and launch date in Section 1 - Provided more detailed description of file format including Dimensions, Variables, and Attributes in Section 2 - Modified the horizontal resolution and clarified the description of the grids in Section 4 - Included version ID in the filename convention described in Section 5.1 - The file sizes were updated in Section 6 to reflect the new horizontal resolution - Improved the description of packing and included directions for unpacking in Section 8 - Two sample programs were added in Section 9 to demonstrate using the HDF library and the HDF-EOS library for reading the data files - Updated the description of First Look Analysis and added a description of Late Look Analysis in Appendix A - Added references for the data format | CCB 3/16/99 |
| Version 4.0 (DAO-1001v4.0) | May 19, 1999 | - Title changed to "File Specification for GEOS-DAS Gridded Output" - Changed details of internal products in Section 1 - Added a figure and description of the horizontal grid structure, removed references to sigma levels in the vertical grid description, and indicated differences in the grids of the CHM products in Section 4 - Indicated that forecast and analysis products will not be archived for distribution by ECS and removed file-naming information for sigma and forecast products in Section 5 - Various changes made to Section 6: - split product table into one table for first look and one for late look - removed sigma products and sigma sizes and definitions - added ESDTs - adjusted the horizontal resolution of CHM products - removed forecast products - added a discussion of the different horizontal and vertical grid structures of the CHM products - Updated the description of First Look Analysis in Appendix A - Added a new table of pressure levels for CHM products and removed the table of sigma levels in Appendix C - Added references for the data format - Levels 36 and 42 in Appendix C tables were changed from 0.1 to 0.2 because in 3D pressure products, 0.2 hPa is now the highest level, changed from 0.1 hPa in earlier documentation | CCB 5/19/99 |
| Version 4.1 (DAO-1001v4.1) | August 18, 1999 | - Slight adjustment of variable content for tavg_cld_p, tavg3d_tmp_p, and tavg3d_tmp_p products. | CCB 8/18/99 |
| Version 4.2 (DAO-1001v4.2) | January 21, 2000 | - Re-write Section 3 to clarify description of time-averaged products. - Changed AM-1 to Terra throughout document. - Added approval dates to revision history for Version 4.0 and Version 4.1. | CCB 1/21/00 |
| Version 4.3 (DAO-1001v4.3) | September 20, 2001 | - In Table 6.1, adjusted the sizes of three products to match the detailed descriptions in Section 6.2: DFLAXENG changes from 66.7 to 58.4 DLLAPCLD changes from 150.1 to 112.6 DLLAPTMP changes from 337.8 to 412.9 | CCB 5/17/00 |
| Version 5.0 DRAFT in support of GEOS-4.x. | November 07, 2001 | -The horizontal resolution of output products has been changed to 288x181. The prior value was 360x181. This change is reflected in Sections 4 and 6. -The grid origin has been changed from (-180.0W,-90.0S) to (0.0W,-90.0S). This change is documented in Section 4. -Adjustments were made to Section 3 to describe the different time-averaging characteristics of the GEOS-4.x system output variables. In particular, 6-hourly time averages now have a different averaging period. This will result in different range begin and end times for 3D pressure products. -In section 6, variables that were unavailable from the GEOS-4.x system were removed from DAS product descriptions. Variables that were previously produced by GEOS-3.x but are no longer available are indicated with a strike-through. Similarly, the old file size calculations are indicated with strike-throughs. -Appendix A was cleaned up to better describe the assimilation modes that are used in the operational arena. -Figures specific to GEOS-3.x were removed. | DDB 10/31/01 |
| Version 5.0 in support of GEOS-4.x (DAO-1001v5.0) | March 20, 2002 | -Time-averaging definitions were changed. All time-averages will be time-stamped with the center of the averaging period. The range time for each time-averaged product will be 00GMT to 00 GMT. This is different from GEOS-3, where products had range times from 21 GMT to 21 GMT. Users will have adjust indices used to read time in order to get data valid for the same time period. -Z0 replaced by Z0H and Z0M in tavg2d_str_x. -GWET in tsyn2d_mis_x was replaced by GWETROOT and GWETTOP in tavg2d_eng_x. -Variable name TGROUND changed to TSKIN in tsyn2d_mis_x and tavg2d_eng_x. -OMEGA moved from tsyn3d_mis_p to tavg3d_mom_p. -Added PRECL to tavg2d_eng_x. PREACC = PRECL + PRECON. -Moved PARDR and PARDF from tavg2d_lsm_x to tavg2d_eng_x. -Removed from tsyn2d_mis_x: ALBEDO, VAVEU, VAVEV, VAVET, TPW, GWET, SNOW -Removed from tsyn3d_mis_p: TKE, OMEGA. -Removed from tavg2d_eng_x: QICE, CT, VAVEQIAU, VAVEQFIL, VAVETIAU. -Removed from tavg2d_str_x: GWDUT, GWDVT, CU, Z0, PIAU. -Removed from tavg2d_lsm_x: SNOWFALL, GREEN, DLWDTC, PARDR, PARDF. -Removed from tavg2d_cld_x: TAULOW, TAUMID, TAUHI, CLDTMP, CLDPRS. -Removed from tavg3d_cld_p: CLDRAS. -Removed from tavg3d_mom_p: RFU, RFV, UIAU, VIAU, DUDT, DVDT. -Removed from tavg3d_mst_p: DQLS, QIAU, QFILL, DQDT. -Removed from tavg3d_tmp_p: TURBT, MOISTT, RADLW, RADSW, GWDT -Added TROPQ, UFLUX, VFLUX, and HFLUX to tsyn2d_mis_x; -PBL replaced by PBLH. | CCB 3/22/02 |
| Version 5.1 (DAO-1001v5.1) | April 25,2002 | The longitude range of the grid was changed from (0 -> 360) to (-180 -> 180). This is consistent with the GEOS-3 products and with ECS conventions. | DDB 04/25/2002 |
| Version 5.2 (DAO-1001v5.2) | May 23, 2002 | -The filename examples in section 5 were updated to reflect the new range times of time-averaged products. -Appendix D was added highlighting the differences between GEOS-3 and GEOS-4 products. | CCB off-line 5/23/2002 |
| Version 5.3 (GMAO-1001v5.3) | February 19, 2004 | - Appendix E added to describe two new ETA-coordinate products. Section 5 modified to add ETA terminology to file and ESDT naming convention. - Data Assimilation Office references changed to Global Modeling and Assimilation Office. - Typo in Section 3 (01:30 changed to 13:30). - Reformatted Appendix D for clarity and included PARDR and PARDF. | CCB, off-line 3/30/2004 |

Table of Contents

1. Introduction	3

2. Format and File Organization	3

2.1 Dimensions	4

2.2 Variables	4

2.3 Global Attributes	6

3. Synoptic vs Time-averaged Products	7

4.  Grid Structure	8

5. File Naming Convention	9

5.1 File Name	9

5.2  Earth Science Data Types (ESDT) Name	11

6. File Collections	13

6.1 File Sizes	13

6.2 Assimilated Synoptic Files	13

6.3 Assimilated Time Averaged Files	16

6.4 Assimilated Chemistry Files	20

7. Metadata	21

7.1 EOSDIS Metadata	21

7.2 COARDS Metadata	21

8.  Sample Software	23

Appendix A. Types of Assimilation Configurations	29

Appendix B. Collection Metadata	30

Appendix C. Vertical Grid Structure	34

Appendix D. Summary of differences between GEOS-3 and GEOS-4	35

Appendix E: Additional products on eta vertical coordinates	38

REFERENCES	42

# 1. Introduction

This document describes the gridded output files from the version of the Goddard EOS Data Assimilation System (GEOS-4), which will support level-4 product generation. The intended audience is EOS instrument teams and other users of GEOS-4 products who need to write software to read GMAO products. The gridded data described in this document will be produced by the GEOS-4 Data Assimilation System (DAS) beginning in 2002 and delivered to the Goddard Distributed Active Archive Center (DAAC), part of the EOSDIS Core System (ECS). Two production suites will run daily, the first-look assimilation and the late-look assimilation (see Appendix A for definitions).  To conserve space, a limited set of products will be generated by the first-look assimilation while the full set will be generated by the late-look assimilation. The product descriptions in Section 6 will identify which products are generated by each run. Information on the status of GMAO product generation can be found at http://gmao.gsfc.nasa.gov/Operations/.

# 2. Format and File Organization

GEOS- 4 files are in HDF-EOS format, which is an extension of the Hierarchical Data Format (HDF), Version 4 developed at the National Center for Supercomputing Applications (NCSA). Each GEOS- 4 file will contain a single HDF-EOS grid, which in turn contains a number of geophysical quantities that we will refer to as "fields" or "variables." Some files will contain 2-D variables on a lon/lat grid and some files will contain 3-D variables on the same lon/lat grid but with an additional vertical dimension. All files will have a time dimension with the number of times dependent on the file type (see Section 6).  GEOS- 4 products always contain one complete day of data.

The variables are created using the GDdeffield function from the HDF-EOS GD API which implements them as HDF Scientific Data Set (SDS) arrays so they can be read with standard HDF routines. In addition to the geophysical variables, the files will have SDS arrays that define dimension scales (or coordinate variables). There will be two distinct scales for each dimension, which will insure that a wide variety of graphical display tools can interpret the dimension scales. In particular, there is a set of dimension scales that adhere to the COARDS conventions (see References).

ECS metadata and other information will be stored as global attributes.

## 2.1 Dimensions

GMAO HDF-EOS files will contain two sets of dimension scale (coordinate) information. One set of dimensions is defined using the SDsetdimscale function of the standard HDF SD interface. This set of scales will have an attribute named "units", set to an appropriate string defined by the COARDS conventions that can be used by applications to identify the dimension. The other set of dimension scales is created using the GDdeffield/GDwritefield functions as suggested in the ECS technical paper "Writing HDF-EOS Grid Products for Optimum Subsetting Services."

Table 2.1-1. Dimension Variables Contained in GMAO HDF-EOS Files

| Name | Description | Type | units attribute |
| --- | --- | --- | --- |
| XDim:EOSGRID | longitude values | float32 | degrees_east |
| YDim:EOSGRID | latitude values | float32 | degrees_north |
| Height:EOSGRID (3D only) | pressure levels | float32 | millibar |
| TIME:EOSGRID | minutes since first time in file | float32 | minutes since YYYY-MM-DD HH:MM:SS |
| XDim | longitude values | float64 | N/A |
| YDim | latitude values | float64 | N/A |
| Height (3D only) | pressure levels | float64 | N/A |
| Time | seconds since 1/1/93 | float64 | N/A |

The 32-bit dimension variables have a "units" attribute that makes them COARDS-compliant, while the 64-bit dimension variables satisfy ECS requirements.

## 2.2 Variables

Variables are stored as SDS arrays even though they are defined with the HDF-EOS GDdeffield function. As a result, one can use the SD interface of the HDF library to read any variable from the file. The only thing one must know is the short name of the variable and the dimensions. You can quickly list the variables in the file by using common utilities such as ncdump or hdp . The latter utility is distributed from NCSA with the HDF library. A sample scan of one GMAO HDF-EOS file is shown below:

unix% hdp dumpsds -h

DAS.flk.asm.tsyn3d_mis_p.GEOS400.1999052800.1999052818.V01 | grep Variable

Variable Name = UWND

Variable Name = VWND

Variable Name = HGHT

Variable Name = TMPU

Variable Name = SPHU

Variable Name = RH

Dimension Variable Name = XDim:EOSGRID

Dimension Variable Name = YDim:EOSGRID

Dimension Variable Name = Height:EOSGRID

Dimension Variable Name = TIME:EOSGRID

Variable Name = XDim

Variable Name = YDim

Variable Name = Height

Variable Name = Time

In Section 8 we will present sample code for reading one or more data fields from this file. The short names for all variables in all GMAO data products are listed in the File Collections chapter, Section 6.

Each variable will have metadata attributes defined that may be useful. Many of these attributes are required by the COARDS conventions while others are for internal GMAO use.  A listing of required attributes follows:

- FillValue (Type = 32-bit floating point or 16-bit signed integer) 
Any missing data will be filled with this value. This attribute is generated automatically by the HDF-EOS library. It will be of the same data type as the variable, thus could be 16-bit integer if the variable is packed.

- long_name (Type = 8-bit signed char) 
Long name or description for this variable.

- units (Type = 8-bit signed char) 
The units of the geophysical variable (ud-units compliant).

- scale_factor (Type = 32-bit floating point) 
If this variable is packed into 16-bit integers, this value would be multiplied to each data value to obtain the floating point number.

- add_offset (Type = 32-bit floating point) 
For a packed variable, add this number after multiplying by the scale_factor.

- missing_value (Type = 32-bit floating point or 16-bit signed integer) 
For an unpacked variable, this is a floating-point representation of the fill value. For a packed variable, this is an integer representation of the fill value.

- fmissing_value (Type = 32-bit floating point) 
Always a floating-point representation of the fill value.

- vmin (Type = 32-bit floating point) 
For internal GMAO use.

- vmax (Type = 32-bit floating point) 
For internal GMAO use.

Since we are not planning to pack the products intended for use by EOS instrument teams, attributes that support packing can be ignored. There may be other attributes that are meant for internal GMAO use that can also be ignored.

## 2.3 Global Attributes

In addition to SDS arrays containing variables and dimension scales, there is additional metadata stored in GMAO HDF-EOS files. Some of this metadata is required by the COARDS conventions, some is present due to ECS requirements, and some may exist as a convenience to internal GMAO users. A summary of global attributes that will exist in all GMAO files follows:

- HDFEOSVersion - Version of the HDF-EOS library used to create this file.

- StructMetadata.0 - This is the GridStructure metadata that is created by the HDF-EOS library.

- CoreMetadata.0 - The ECS inventory metadata.

- ArchivedMetadata.0 - The ECS archive metadata.

- Title - GEOS-DAS Version number and CVS tag.

- Conventions - Should always be set to "COARDS".

- Source - NASA Global Modeling and Assimilation Office, GEOS-DAS Version.

- Contact - Where to send questions.

History - Version of DAS output library.

# 3. Synoptic vs Time-averaged Products

GEOS-4 gridded output files are identified as either synoptic or time-averaged products. Synoptic products are defined in Section 6.2 while time-averaged products are defined in Section 6.3. Additional synoptic products associated with the ozone assimilation are defined in Section 6.4. All synoptic products contain fields that are snapshots of a specific time.  The synoptic products defined in Section 6.2 are generated directly from the atmospheric data analysis, which is performed every six hours at the four synoptic times (00 GMT, 06 GMT, 12 GMT, and 18 GMT). The "tsyn3d_mis_p" product has a time frequency of 6 hours, with data for each synoptic time. The "tsyn2d_mis_x" synoptic product has a time-frequency of 3 hours. The values for 03 GMT, 09 GMT, 15 GMT, and 21 GMT are time-interpolated from the synoptic times.  This is done to make the product consistent with GEOS-3 products.

Time-averaged products are averaged over a 3-hour period for single level files or a 6-hour period for pressure level files.  Single level products contain 8 times, with time-stamps of 01:30, 04:30, 07:30, 10:30, 13:30, 16:30, 19:30, and 22:30 GMT.  Each time-stamp represents the center of a three-hour average, i.e., the first time in each file (time stamped with 01:30 GMT) represents the average between 00 GMT and 03 GMT.  Time-averaged pressure level products contain 4 times with time-stamps of 03, 09, 15, and 21 GMT.  Each time-stamp represents the center of a 6-hour average, i.e., the first time in the file (time-stamped with 03 GMT) represents an average between  00 GMT and 06 GMT.  The valid range time of a daily file is 00 GMT to 00 GMT for both 3-hour and 6-hour average products.  Note that the time-averaging of GEOS-4 products is different from the preceding GEOS-3 system (see diagram).    Also note that eta-level products, added to the GEOS-4 product suite in 2004, have a different time-averaging convention.  Please see Appendix E for details.

# 4.  Grid Structure

Most GEOS-4 gridded output will be on a 1.25 x 1.0 degree global longitude-latitude horizontal grid (288,181). Products from the GMAO ozone assimilation (D4FAXCHM, D4FAPCHM, D4LAXCHM, D4LAPCHM) will be on a 2.5 x 2.0 degree longitude-latitude horizontal grid (144,91). The horizontal grid origin is the lower-left point and represents the geolocation (-180.0 W, -90.0 S). Latitude or longitude as a function of the index can be determined by:

lon = -180 + (x-1) * dx

lat = -90 + (y-1) * dy

where dx = 1.25, dy = 1.0 except in the case of ozone products where dx = 2.5, dy = 2.0. For all parameters of each file, the gridpoints represent the center of a box, i.e., the value at (lon=5,lat=0) represents a box bounded by the points (lon=4.375,lat=-0.5), (lon=5.625,lat=0.5), (lon=5.625,lat=0.5), and (lon=4.375,lat=-0.5).  Scalar values are the volume mean within the box.

The vertical structure of gridded products will have 3 different configurations: single-level (can be vertical averages), pressure levels, or eta levels (discussed in Appendix E). Single level data for a given variable appear as 3-dimensional fields (x,y,time) while pressure level data appear as 4-dimensional fields (x,y,z,time). Pressure level data will be output on 36 pressure levels (hPa), except for D4FAPCHM and D4LAPCHM which will have 42 pressure levels (see Appendix C). The appropriate grid structure will be specified both in the filename and the metadata.

# 5. File Naming Convention

Each GEOS-4 product will have a complete file name identified in the EOSDIS metadata as "LocalGranuleID". EOSDIS also requires abbreviated naming indices (8-character limit) for each Earth Science Data Type (ESDT). The ESDT indices convention is described in section 5.2.

## 5.1 File Name

The standard generic complete name for the assimilated GEOS- 4 configuration products will appear as follows:

DAS.config.mode.filetype.expid.yyyymmddhh.yyyymmddhh.version

A brief description of the node fields appear below:

DAS:

Identifies output as a Data Assimilation System product.

config:

GEOS-4 will run in two different configurations. Appendix A describes these configurations. These are the strings that can appear in the config field.

flk - First Look

llk - Late Look

mode:

GEOS-4 can run in different modes of operation, but the only mode used to support EOS instrument teams is "asm".

asm - Assimilation. Uses a combination of atmospheric data analysis and model forecasting to generate a time-series of global atmospheric quantities.

filetype:

The major filetypes are subdivided into file collections. Collections contain several fields with common characteristics. These collections are necessary to keep file sizes reasonable. Each filetype will contain the following information:

type/dimension_group_level

type/dimension:

There exist four possible type/dimension conventions for the DAS data products:

tsyn2d - 2-dimensional instantaneous fields at synoptic times (no time averaging).

tsyn3d - 3-dimensional instantaneous fields at synoptic times (no time averaging).

tavg2d - 2-dimensional 3-hour time averaged fields, time-stamped at the center of the averaging period. For example, 04:30z output would be a 3z-6z time average).

tavg3d - 3-dimensional 6-hour time averaged fields, time-stamped at the center of the averaging period.  For example, 3z output would be a 0z-6z time average.

group (for files which contain 2-dimensional fields):

str: stress related fields

eng: energy related fields

cld: cloud related fields

lsm: land surface model related fields

chm: chemical related fields (e.g. ozone)

mis: mixture of prognostic and diagnostic fields

group (for files which contain 3-dimensional fields):

mis: mixture of prognostic and diagnostic fields

mom: momentum profile fields

tmp: temperature profile fields

mst: moisture profile fields

cld: cloud profile related fields

trp: transport profile fields (e.g. eddy diffusivity)

chm: chemical profile fields

level: There are three possible level types for the DAS data:

x: single level data (surface, column integrated, single level)

p: pressure level data (see Appendix C for pressure levels)

e: ETA level data (see Appendix E)

expid:

Experiment Identification. The GEOS-4 DAS data sets will be labeled:

GEOS4##

where ## is a two-digit number.  At the time of this document’s release, the experiment identification is GEOS403.  When GEOS-4 was initialized in operations, the experiment identification was GEOS401.  When a reprocessing experiment is run over previously processed data periods or when a patched version is put into First-look or Late-look operations, we will increment the ## sequentially.  Note that products produced by GEOS-3 had an experiment identification of AM101.  These First-look and Late-look products were generated between January 1, 2000 and the operations date of GEOS-4 (October 1, 2002).  As updated versions of the GEOS software are implemented in operations, the cvs tag in the metadata parameter "Title" will be modified as well as the GMAO operations status web page (http://gmao.gsfc.nasa.gov/Operations/).

yyyymmddhh.yyyymmddhh:

This group defines the beginning date and synoptic time as well as the ending date and synoptic time.

yyyy - year string (e.g. "2002")

mm - month string (e.g. "09" for September)

dd - day of the month string (e.g. "10" for the tenth day of the month)

hh - time (synoptic hour, e.g. "18" for 18:00 Greenwich Mean Time)

version:

This group defines the file version and takes the form V##. Under normal conditions ## will be 01. In the event of a processing error that requires a re-processing, this number will be incremented to identify the new version of this file. The file version will also be represented in the EOSDIS metadata as "LocalVersionID".

EXAMPLE:

DAS.flk.asm.tavg3d_mom_p.GEOS401.2002091500.2002091600.V01

This is an example of a DAS filename.  It is a first look assimilation product. The data are 6-hour time averaged output on pressure levels (3 dimensions). The filetype consists of momentum fields. The valid range time for the file is Sep 15 at 00 GMT through Sep 16 at 00 GMT.  There are 4 times, each representing a 6-hour average.  The first average is from 00 GMT to 06 GMT.  The last average is from 18 GMT to 00 GMT.  See the discussion on time-averaged data in section 3 for more information.

## 5.2  Earth Science Data Types (ESDT) Name

To accommodate EOSDIS toolkit requirements, GEOS-4 complete filenames are associated to shorter or abbreviated indices in the ESDTs. EOSDIS requires a short (8 character) name for each ESDT. Below is the abbreviated naming convention for the GEOS-4 gridded ESDTs. The standard ESDT naming convention for the GEOS-4 gridded output will have the form:

DSPMVCCC

D: DAS identifier. Always D.

S: Major system number.  For GEOS-4, 4.

P: Product

F = First Look

L = Late Look

M: Mode

A = Assimilation

F = Forecast (currently not used)

V: Vertical Coordinate:

X = Single-Level

P = Pressure

E = ETA (Appendix E)

CCC: Filetype

MIS = misc

ENG = energy

LSM = land surface model

STR = stress

CHM = chemical

CLD = cloud

MOM = momentum

MST = moisture

TMP = temperature

TRP = transport fields

Example:

Abbreviated Name: D4FAPMOM

Complete Name: DAS.flk.asm.tavg3d_mom_p.GEOS401.2002091500.2001091600.V01

# 6. File Collections

The contents of the Data Assimilation System file collections are described in sections 6.2, 6.3 and 6.4 while the sizes of each file are discussed in Section 6.1.

## 6.1 File Sizes

With the exception of chemistry (chm) products, GEOS-4 HDF files contain 1 day of data on a 1.25 degree x 1 degree lon-lat grid using 32-bit floating-point storage. Chm products are stored on a 2.5 degree by 2.0 degree lon-lat grid. See Appendix C for details about vertical levels. File sizes are approximate as metadata can cause slight variations in file size.

| First-Look Filetype Group | Single Level (MB/day) (288,181,1) 8X/day | Pressure Levels (MB/day) (288,181,36) 4X/day | Eta Layers (MB/day) (288,181,55/24) 4X/day see appendix E |
| --- | --- | --- | --- |
| mis | 31.7 (D4FAXMIS) | 180.2 (D4FAPMIS) | 551.6 (D4FAEMIS) |
| eng | 51.7 (D4FAXENG) | N/A | N/A |
| str | 21.7 (D4FAXSTR) | N/A | N/A |
| chm | 0.4 (D4FAXCHM) * | 8.8 (D4FAPCHM) ** | N/A |
| cld | 15.0 (D4FAXCLD) | Not produced | N/A |
| lsm | 11.7 (D4FAXLSM) | N/A | N/A |
| mom | N/A | Not produced | N/A |
| mst | N/A | Not produced | N/A |
| tmp | N/A | Not produced | N/A |
| trp | N/A | Not produced | 362.1 (D4FAETRP) |
| Totals | 132.2 | 189.0 | 912.6 |

| Late-Look Filetype Group | Single Level (MB/day) (288,181,1) 8X/day | Pressure Levels (MB/day) (288,181,36) 4X/day | Eta Layers (MB/day) (288,181,55/24) 4X/day see appendix E |
| --- | --- | --- | --- |
| mis | 31.7 (D4LAXMIS) | 180.2 (D4LAPMIS) | 551.6 (D4LAEMIS) |
| eng | 51.7 (D4LAXENG) | N/A | N/A |
| str | 21.7 (D4LAXSTR) | N/A | N/A |
| chm | 0.4 (D4LAXCHM) * | 8.8 (D4LAPCHM) ** | N/A |
| cld | 15.0 (D4LAXCLD) | 90.1 (D4LAPCLD) | N/A |
| lsm | 11.7 (D4LAXLSM) | N/A | N/A |
| mom | N/A | 150.2 (D4LAPMOM) | N/A |
| mst | N/A | 60.1 (D4LAPMST) | N/A |
| tmp | N/A | 150.2 (D4LAPTMP) | N/A |
| trp | N/A | 120.1 (D4LAPTRP) | 362.1 (D4LAETRP) |
| Total | 132.2 | 759.7 | 912.6 |

* = (144, 91, 1) ** = (144, 91, 42)

## 6.2 Assimilated Synoptic Files

Below are the variables that are output into each syn file. These are instantaneous fields (no time averaging). The approximate size of each file below is determined by the following:

A x B x C x D x E x F = bytes/day

where:

A: X-Dimension

B: Y-Dimension

C: Vertical dimension

D: Number of fields in file

E: Number of times in file

F: Number of bytes per floating point number

The method for calculating sizes is the same in 6.2, 6.3, and 6.4.

NOTE: All HDF variable names are UPPERCASE.

- tsyn2d_mis_x (8 times per day)

First-look ECS short name: D4FAXMIS

First-look ECS long name: DAS First-look 2d state (miscellaneous), instantaneous

Late-look ECS short name: D4LAXMIS

Late-look ECS long name: DAS Late-look 2d state (miscellaneous), instantaneous

Size: 288 x 181 x 1 x 19 x 8 x 4 = 31.7 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| PHIS | Surface geopotential | (m/s)2 |
| PS | Surface pressure | hPa |
| SLP | Sea level pressure | hPa |
| SURFTYPE | Surface types | 0=water, 1=land, 2=ice |
| TSKIN | Skin temperature | K |
| T2M | Temperature at 2 m above surface | K |
| T10M | Temperature at 10 m above surface | K |
| Q2M | Specific humidity at 2 m above surface | g/kg |
| Q10M | Specific humidity at 10 m above surface | g/kg |
| U2M | Zonal wind at 10 m above surface | m/s |
| V2M | Meridional wind at 2 m above surface | m/s |
| U10M | Zonal wind at 10 m above surface | m/s |
| V10M | Meridional wind at 10 m above surface | m/s |
| UFLUX | Zonal wind surface stress | N/m2 |
| VFLUX | Meridional wind surface stress | N/m2 |
| HFLUX | Sensible heat flux (pos. upward) | W/m2 |
| TROPP | Tropopause pressure | hPa |
| TROPT | Tropopause temperature | K |
| TROPQ | Tropopause specific humidity | g/kg |

- tsyn3d_mis_p (4 times per day)

First-look ECS short name: D4FAPMIS

First-look ECS long name: DAS First-look 3d state (miscellaneous), instantaneous on pressure coordinates

Late-look ECS short name: D4LAPMIS

Late-look ECS long name: DAS Late-look 3d state (miscellaneous), instantaneous on pressure coordinates

Size: 288 x 181 x 36 x 6 x 4 x 4 = 180.2 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| UWND | Zonal wind | m/s |
| VWND | Meridional wind | m/s |
| HGHT | Geopotential height (virtual) | m |
| TMPU | Temperature | K |
| SPHU | Specific humidity | g/kg |
| RH | Relative humidity | percent |

## 6.3 Assimilated Time Averaged Files

Below are the variables that are output in each "tavg" file. These are time-averaged fields. Single-level, or 2-dimensional data will be output every 3 hours while 3-dimensional data will be output every 6 hours.

- tavg2d_eng_x (8 times per day)

First-look ECS short name: D4FAXENG

First-look ECS long name: DAS First-look 2d energy, averaged

Late-look ECS short name: D4LAXENG

Late-look ECS long name: DAS Late-look 2d energy, averaged

Size: 288 x 181 x 1 x 31 x 8 x 4 = 51.7 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| PREACC | Total precipitation rate | mm/day |
| PRECL | Large-scale precipitation rate | mm/day |
| PRECON | Convective precipitation rate | mm/day |
| TPW | Total precipitable water | g/cm2 |
| EVAP | Surface evaporation | mm/day |
| GWETROOT | Root zone soil wetness | fraction |
| GWETTOP | Top soil layer wetness | fraction |
| HFLUX | Sensible heat flux (positive upward) | W/m2 |
| TSKIN | Skin temperature | K |
| T2M | Temperature interpolated to 2 meters | K |
| T10M | Temperature interpolated to 10 meters | K |
| Q2M | Specific humidity interpolated to 2 meters | g/kg |
| Q10M | Specific humidity interpolated to 10 meters | g/kg |
| RADLWG | Net upward longwave flux at the ground | W/m2 |
| RADSWG | Net downward shortwave flux at the ground | W/m2 |
| PARDF | Diffuse-beam photosynthetically active radiation | W/m2 |
| PARDR | Direct-beam photosynthetically active radiation | W/m2 |
| LWGCLR | Clear sky net longwave flux at the ground | W/m2 |
| SWGCLR | Clear sky net downward shortwave radiation at the ground | W/m2 |
| ALBEDO | Surface albedo | fraction |
| ALBVISDR | Direct beam VIS surface albedo | fraction |
| ALBVISDF | Diffuse beam VIS surface albedo | fraction |
| ALBNIRDR | Direct beam NIR surface albedo | fraction |
| ALBNIRDF | Diffuse beam NIR surface albedo | fraction |
| VAVEU | Vertically averaged zonal wind | m/s |
| VAVEV | Vertically averaged meridional wind | m/s |
| VAVET | Vertically averaged temperature | K |
| VAVEUQ | Vertically averaged UWND*SPHU | m-g/s-kg |
| VAVEVQ | Vertically averaged VWND*SPHU | m-g/s-kg |
| VAVEUT | Vertically averaged UWND*TMPU | m-K/s |
| VAVEVT | Vertically averaged VWND*TMPU | m-K/s |

- tavg2d_str_x (8 times per day)

First-look ESDT: D4FAXSTR

First-look ECS long name: DAS First-look 2d stress, averaged

Late-look ECS short name: D4LAXSTR

Late-look ECS long name: DAS Late-look 2d stress, averaged

Size: 288 x 181 x 1 x 13 x 8 x 4 = 21.7 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| PS | Time averaged surface pressure | hPa |
| UFLUX | Zonal wind surface stress | N/m2 |
| VFLUX | Meridional wind surface stress | N/m2 |
| GWDUS | Zonal wind gravity wave surface stress | N/m2 |
| GWDVS | Meridional wind gravity wave surface stress | N/m2 |
| USTAR | Friction velocity | m/s |
| Z0H | Roughness length, sensible heat | m |
| Z0M | Roughness length, momentum | m |
| PBLH | Planetary boundary layer height | m |
| U2M | Zonal wind interpolated to 2 meters | m/s |
| V2M | Meridional wind interpolated to 2 meters | m/s |
| U10M | Zonal wind interpolated to 10 meters | m/s |
| V10M | Meridional wind interpolated to 10 meters | m/s |

- tavg2d_lsm_x (8 times per day)

First-look ESDT: D4FAXLSM

First-look ECS long name: DAS First-look 2d Land Surface Model (LSM), averaged

Late-look ECS short name: D4LAXLSM

Late-look ECS long name: DAS Late-look 2d Land Surface Model (LSM), averaged

Size: 288 x 181 x 1 x 7 x 8 x 4 = 11.7 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| RAINCON | Convective rainfall (liquid precipitate) | mm/day |
| RAINLSP | Large-scale rainfall (liquid precipitate) | mm/day |
| LWGDOWN | Downward longwave radiation at the ground | W/m2 |
| LWGUP | Upward longwave radiation at the ground | W/m2 |
| LAI | Leaf area index | percent |
| DTG | Total change in ground temperature | K/s |
| SNOW | Snow depth | mm (water equivalent) |

- tavg2d_cld_x (8 times per day)

First-look ESDT: D4FAXCLD

First-look ECS long name: DAS First-look 2d cloud, averaged

Late-look ECS short name: D4LAXCLD

Late-look ECS long name: DAS Late-look 2d cloud, averaged

Size: 288 x 181 x 1 x 9 x 8 x 4 = 15.0 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| OLR | Outgoing longwave radiation | W/m2 |
| OLRCLR | Clear sky outgoing longwave radiation | W/m2 |
| RADSWT | Incident shortwave radiation at top of atmosphere | W/m2 |
| OSR | Outgoing shortwave radiation | W/m2 |
| OSRCLR | Clear sky outgoing shortwave radiation | W/m2 |
| CLDFRC | Total cloud fraction | fraction |
| CLDLOW | Low-level (1000-700 hPa) cloud fraction | fraction |
| CLDMID | Mid-level (700-400 hPa) cloud fraction | fraction |
| CLDHI | High-level (above 400 mb) cloud fraction | fraction |

- tavg3d_cld_p (4 times per day)

Late-look ECS short name: D4LAPCLD

Late-look ECS long name: DAS Late-look 3d cloud, averaged on pressure coordinates

Size: 288 x 181 x 36 x 3 x 4 x 4 = 90.1 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| TAUCLI | Cloud optical depth, ice | non-dimensional |
| TAUCLW | Cloud optical depth, water | non-dimensional |
| CLDTOT | 3-D total cloud fraction | fraction |

- tavg3d_mom_p (4 times per day)

Late-look ECS short name: D4LAPMOM

Late-look ECS long name: DAS Late-look 3d momentum, averaged on pressure coordinates

Size: 288 x 181 x 36 x 5 x 4 x 4 = 150.2 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| TURBU | Zonal wind tendency due to turbulence | m/s/day |
| TURBV | Meridional wind tendency due to turbulence | m/s/day |
| GWDU | Zonal wind tendency due to gravity wave drag | m/s/day |
| GWDV | Meridional wind tendency due to gravity wave drag | m/s/day |
| OMEGA | Vertical velocity | Pa/s |

- tavg3d_mst_p (4 times per day)

Late-look ECS short name: D4LAPMST

Late-look ECS long name: DAS Late-look 3d moisture, averaged on pressure coordinates

Size: 288 x 181 x 36 x 2 x 4 x 4 = 60.1 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| TURBQ | Specific humidity tendency due to turbulence | g/kg/day |
| MOISTQ | Specific humidity tendency due to moist processes | g/kg/day |

- tavg3d_tmp_p (4 times per day)

Late-look ECS short name: D4LAPTMP

Late-look ECS long name: DAS Late-look 3d temperature, averaged on pressure coordinates

Size: 288 x 181 x 36 x 5 x 4 x 4 = 150.2 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| TURBT | Temperature tendency due to turbulence | K/day |
| MOISTT | Temperature tendency due to moist processes | K/day |
| RADLW | Temperature tendency due to longwave radiation | K/day |
| RADSW | Temperature tendency due to shortwave radiation | K/day |
| GWDT | Temperature tendency due to gravity wave drag | K/day |

- tavg3d_trp_p (nominally 4 times per day)

Late-look ECS short name: D4LAPTRP

Late-look ECS long name: DAS Late-look 3d transport, averaged on pressure coordinates

Size: 288 x 181 x 36 x 4 x 4 x 4 = 120.1 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| KH | Eddy diffusivity coefficient for scalars | m2/s |
| KM | Eddy diffusivity coefficient for momentum | m2/s |
| CLDMAS | Cloud mass flux | kg/m2/s |
| DTRAIN | Detrainment cloud mass flux | kg/m2/s |

## 6.4 Assimilated Chemistry Files

The following variables are generated by the GMAO Ozone Assimilation System. These are instantaneous fields (no time averaging). These products are produced from an offline (OL) ozone assimilation, which uses the wind data from the DAS as input. The ozone assimilation operates at a coarser resolution than the DAS, thus these products have horizontal resolution of 2.5 x 2 degrees. In addition, the vertical structure of the 3-D ozone products is different than other 3-D DAS products. See Appendix C for details.

The ozone mixing ratio fields in the tavg3d_chm_p product at the following levels: 1000, 975, 950, 925, 900, and 875 hPa are provided at the request of users. The ozone values provided at these levels are identical to the values at 850 hPa. Ozone data are assimilated between 850 and 0.2 hPa. No geophysical significance should be attributed to the 1000, 975, 950, 915, 900, and the 875 hPa levels.

- tsyn2d_chm_x (8 times per day)

First-look ECS short name:  D4FAXCHM

First-look ECS long name: DAS First-look 2d chemistry, instantaneous

Late-look ECS short name: D4LAXCHM

Late-look ECS long name: DAS Late-look 2d chemistry, instantaneous

Size: 144 x 91 x 1 x 1 x 8 x 4 = 0.4 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| OZONE | Total ozone | DU |

- tsyn3d_chm_p (4 times per day)

First-look ECS short name:  D4FAPCHM

First-look ECS long name: DAS First-look 3d chemistry, instantaneous on pressure coordinates

Late-look ECS short name: D4LAPCHM

Late-look ECS long name: DAS Late-look 3d chemistry, instantaneous on pressure coordinates

Size:  144 x 91 x 42 x 1 x 4 x 4 = 8.8 MB/day

| Variable Name | Description | Units |
| --- | --- | --- |
| OZONE | Ozone mixing ratio | ppmv |

# 7. Metadata

GEOS-4 gridded output files will be associated with two types of metadata. Depending on the utility you use to access the file, one set of metadata will be read and the other ignored.

## 7.1 EOSDIS Metadata

If you are using the EOSDIS toolkit you will only use the EOSDIS metadata. EOSDIS identifies two major types of metadata, collection and granule.

Collection metadata are stored in a separate index file. This file is like a library card catalog. Each ESDT has a "card" that contains its unique collection attributes. Appendix B describes the ESDT collection metadata.

Granule metadata is the "table of contents" information stored on the data file itself. The EOSDIS granule metadata include:

- file name (local granule ID)

- grid structure

- number of times per day fields are stored in this file

- number of vertical levels for each variable in this file

- names of variables in this file

- variable format (32-bit floating point, 16-bit integer, etc.)

- variable storage dimensions

2-d fields will have 3 storage dimensions, time, latitude and longitude

3-d fields will have 4 storage dimensions, time, latitude, longitude and vertical levels

- "missing" value for each variable

- unpacking scale factor for each packed variable (see section 8)

- unpacking off-set value for each packed variable (see section 8)

## 7.2 COARDS Metadata

If you use GRADS or FERRET to view GEOS-4 gridded data sets you will only use the COARDS metadata. These metadata will comply with the COARDS convention and include the following information:

- space-time grid information (dimension variables)

- variable long names (descriptions)

- variable units

- "missing" value for each variable

- unpacking scale factor for each packed variable (see section 8)

unpacking off-set value for each packed variable (see section 8)

# 8.  Sample Software

Presented here is software that illustrates using the standard HDF library or the ECS HDF-EOS library to read GEOS-4 products. The program shown below will accept as command line arguments a file name and a field name. It will open the file, read the requested field at the first time, compute an average for this field, and print the result to standard output. There are two versions of this program. The first version uses the HDF-EOS library to read the file. The second version uses the standard HDF library to read the file. Electronic copies of these programs can be obtained from the Operations section of the GMAO web page:

http://gmao.gsfc.nasa.gov/Operations/

/****************************************************************************/

/* This program demonstrates how to read a field from a GMAO HDF-EOS */

/* product using the HDF-EOS library. It will take a file name and */

/* field name on the command line, read the first time of the given */

/* field, calculate an average of that time and print the average. */

/* */

/* usage: avg <file name> <field name> */

/* */

/* Rob Lucchesi */

/* rlucchesi@GMAO.gsfc.nasa.gov */

/* 2/12/1999 */

/****************************************************************************/

#include "hdf.h"

#include "mfhdf.h"

#include <stdio.h>

#define XDIM 288

#define YDIM 181

#define ZDIM 36

main(int argc,char *argv[]) {

int32 sd_id, sds_id, status;

int32 sds_index;

int32 start[4], edges[4], stride[4];

char *fname, *vname;

float32 data_array[ZDIM][YDIM][XDIM];

float32 avg, sum;

int32 i,j,k;

int32 file_id, gd_id;

if (argc != 3) {

printf("Usage: avg <filename> <field> \n");

exit (-1);

}

fname = argv[1];

vname = argv[2];

/* Open the file (read-only) */

file_id = GDopen (fname, DFACC_RDONLY);

if (file_id < 0) {

printf ("Could not open %s\n",fname);

exit(-1);

}

/* Attach to the EOS grid contained within the file. */

/* The GMAO uses the generic name "EOSGRID" for the grid in all products. */

gd_id = GDattach (file_id,"EOSGRID");

if (gd_id < 0) {

printf ("Could not open %s\n",fname);

exit(-1);

}

/* Set positioning arrays to read the entire field at the first time. */

start[0] = 0;

start[1] = 0;

start[2] = 0;

start[3] = 0;

stride[0] = 1;

stride[1] = 1;

stride[2] = 1;

stride[3] = 1;

edges[0] = 1;

edges[1] = ZDIM;

edges[2] = YDIM;

edges[3] = XDIM;

/*

In this program, we read the entire field. By manipulating the start

and edges arrays, it is possible to read a subset of the entire array.

For example, to read a 3D section defined by x=100,224; y=50,149;

z=15,16 you would set the start and edges arrays to the following:

start[0] = 0; time start location

start[1] = 15; z-dim start location

start[2] = 50; y-dim start location

start[3] = 100; x-dim start location

edges[0] = 1; time length

edges[1] = 2; z-dim length

edges[2] = 100; y-dim length

edges[3] = 125; x-dim length

*/

/* Read the data into data_array */

status = GDreadfield (gd_id, vname, start, stride, edges, data_array);

printf ("Read status=%d\n",status);

/* Calculate and print the average */

sum=0.0;

for (i=0; i<XDIM; i++)

for (j=0; j<YDIM; j++)

for (k=0; k<ZDIM; k++)

sum += data_array[k][j][i];

avg = sum/(XDIM*YDIM*ZDIM);

printf ("Average of %s in 3 dimensions is=%f\n",vname,avg);

/* Close file. */

status = GDdetach (gd_id);

status = GDclose (file_id);

}

/****************************************************************************/

/* This program demonstrates how to read a field from a GMAO HDF-EOS */

/* product using the HDF library (HDF-EOS not required). It will take */

/* a file name and field name on the command line, read the first time */

/* of the given field, calculate an average of that time and print the average. */

/* */

/* usage: avg <file name> <field name> */

/* */

/* Rob Lucchesi */

/* rlucchesi@gmao.gsfc.nasa.gov */

/* 2/12/1999 */

/****************************************************************************/

#include "hdf.h"

#include "mfhdf.h"

#include <stdio.h>

#define XDIM 288

#define YDIM 181

#define ZDIM 36

main(int argc,char *argv[]) {

int32 sd_id, sds_id, status;

int32 sds_index;

int32 start[4], edges[4], stride[4];

char *fname, *vname;

float32 data_array[ZDIM][YDIM][XDIM];

float32 avg, sum;

int32 i,j,k;

if (argc != 3) {

printf("Usage: avg <filename> <field> \n");

exit (-1);

}

fname = argv[1];

vname = argv[2];

/* Open the file (read-only) */

sd_id = SDstart (fname, DFACC_RDONLY);

if (sd_id < 0) {

printf ("Could not open %s\n",fname);

exit(-1);

}

/* Find the index and ID of the SDS for the given variable name. */

sds_index = SDnametoindex (sd_id, vname);

if (sds_index < 0) {

printf ("Could not find %s\n",vname);

exit(-1);

}

sds_id = SDselect (sd_id,sds_index);

/* Set positioning arrays to read the entire field at the first time. */

start[0] = 0;

start[1] = 0;

start[2] = 0;

start[3] = 0;

stride[0] = 1;

stride[1] = 1;

stride[2] = 1;

stride[3] = 1;

edges[0] = 1;

edges[1] = ZDIM;

edges[2] = YDIM;

edges[3] = XDIM;

/*

In this program, we read the entire field. By manipulating the start

and edges arrays, it is possible to read a subset of the entire array.

For example, to read a 3D section defined by x=100,224; y=50,149;

z=15,16 you would set the start and edges arrays to the following:

start[0] = 0; time start location

start[1] = 15; z-dim start location

start[2] = 50; y-dim start location

start[3] = 100; x-dim start location

edges[0] = 1; time length

edges[1] = 2; z-dim length

edges[2] = 100; y-dim length

edges[3] = 125; x-dim length

*/

/* Read the data into data_array */

status = SDreaddata (sds_id, start, stride, edges, (VOIDP) data_array);

printf ("read status=%d\n",status);

/* Calculate and print the average */

sum=0.0;

for (i=0; i<XDIM; i++)

for (j=0; j<YDIM; j++)

for (k=0; k<ZDIM; k++)

sum += data_array[k][j][i];

avg = sum/(XDIM*YDIM*ZDIM);

printf ("Average of %s in 3 dimensions is=%f\n",vname,avg);

/* Close file. */

status = SDendaccess (sds_id);

status = SDend (sd_id);

}

# Appendix A. Types of Assimilation Configurations

First Look Assimilation. Atmospheric observations from satellites, balloons, aircraft, ships, and other sources are grouped into six-hour data windows and processed by the atmospheric analysis four times each day. The first look analysis will run 6 to 10 hours after the 4 analysis times (0Z, 6Z, 12Z, 18Z). It will run using whatever conventional and satellite observations are available at the data cut-off time. Even though first-look will run as 4 distinct segments, the GMAO will only distribute products that contain one complete day. Products produced from this and any other assimilation are a combination of output from the statistical analysis system and a short GCM forecast.

Late Look Assimilation. The software configuration is identical to the first look assimilation but, due to a delay of at least two weeks, a more complete set of input observations can be used. Unlike the first look analysis, the late look analysis will process one day at a time. The late look assimilation produces a greater volume of output products, since computational performance is not as critical.

Forecast/Simulation. This is a GCM forecast, with no insertion of atmospheric data via the analysis. The only outside data that enters the system are the boundary conditions, i.e., sea surface temperature and sea-ice concentration. Five-day forecasts are typically generated to support NASA field campaigns and to assess assimilation and forecast skill. Multi-year simulations are produced to investigate the climatology of the GCM. GMAO forecast products are not distributed to ECS and file formats are not discussed in this document.

Reprocessing. The GMAO will reprocess specified time periods since EOS-Terra launch using a recent version of the GEOS DAS software to support instrument team reprocessing requirements. A reprocessing run will use the Late Look assimilation file groupings and will use a version of GEOS DAS that is held constant through the reprocessing period. It is expected that new ECS ESDTs will be generated for each reprocessing run.

Reanalysis. The GMAO will occasionally run reanalysis experiments. Reanalysis is the same as reprocessing except the time period is often much longer and not necessarily part of the EOS period. Reanalysis experiments are often run using baseline versions of the GEOS DAS system to support a wide variety of research activities internal and external to the GMAO. Unique ESDTs will be generated for any reanalysis data distributed through ECS.

# Appendix B. Collection Metadata

GEOS-4 collection metadata will contain the following.  To view the ESDTs associated with GMAO products, which include collection metadata, see the GMAO Operations web page: http://gmao.gsfc.nasa.gov/Operations.

ECS Collection

Revision Date

Suggested Usage

Single Type Collection

Collection State

Maintenance and Update Frequency

Spatial

Spatial Coverage Type

Bounding Rectangle

West Bounding Coordinate

North Bounding Coordinate

East Bounding Coordinate

South Bounding Coordinate

Altitude System Definition (for 3d files only)

Altitude Datum Name

Altitude Distance Units

Altitude Encoding Method

Altitude Resolution Class

Altitude Resolution

Depth System Definition (land surface files only)

Depth Datum Name

Depth Distance Units

Depth Encoding Method

Depth Resolution Class

Depth Resolution

Geographic Coordinate System

Latitude Resolution

Longitude Resolution

Geographic Coordinate Units

Temporal

Time Type

Date Type

Temporal Range Type

Precision of Seconds

Ends at Present Flag

Range Date Time

Range Beginning Date

Range Beginning Time

Range Ending Date

Range Ending Time

Contact Person

Role

Hours of Service

Contact Job Position

Contact First Name

Contact Middle Name

Contact Last Name

Contact Person Address

Street address

City

State/Province

Postal Code

Country

Telephone

Telephone Container

Telephone Number

Telephone Number Type

Email

Electronic Mail Address

Contact Organization

Role

Hours of Service

Contact Instruction

Contact Organization Name

Contact Organization Address

Street Address

City

State/Province

Postal Code

Country

Organization Telephone Number

Telephone Number

Telephone Number Type

Organizational Email

Electronic Mail Address

Discipline Topic Parameters

ECS Discipline Keyword

ECS Topic Keyword

ECS Term Keyword

ECS Variable Keyword

ECS Parameter Keyword

Temporal Keyword Class

Temporal Keyword

Spatial Keyword Class

Spatial Keyword

Processing Level

Processing Level Description

Processing Level ID

Analysis Source

Analysis Short Name

Analysis Long Name

Analysis Technique

Analysis Type

CSDT Description

Primary CSDT

Additional Attributes

Additional Attribute Data Type

Additional Attribute Description

Additional Attribute Name

Physical Parameter Details

Parameter Units of Measure

Parameter Range

Parameter Value Accuracy

Parameter Value Accuracy Explanation

Parameter Measurement Resolution

Storage Medium Class (filled in by DAAC)

Storage Medium

# Appendix C. Vertical Grid Structure

Pressure level data will be output on the following 36 pressure levels for all 3-D products except chemistry:

| Level | Pressure (hPa) | Level | Pressure (hPa) | Level | Pressure (hPa) |
| --- | --- | --- | --- | --- | --- |
| 1 | 1000 | 13 | 600 | 25 | 50 |
| 2 | 975 | 14 | 550 | 26 | 40 |
| 3 | 950 | 15 | 500 | 27 | 30 |
| 4 | 925 | 16 | 450 | 28 | 20 |
| 5 | 900 | 17 | 400 | 29 | 10 |
| 6 | 875 | 18 | 350 | 30 | 7 |
| 7 | 850 | 19 | 300 | 31 | 5 |
| 8 | 825 | 20 | 250 | 32 | 3 |
| 9 | 800 | 21 | 200 | 33 | 2 |
| 10 | 750 | 22 | 150 | 34 | 1 |
| 11 | 700 | 23 | 100 | 35 | 0.4 |
| 12 | 650 | 24 | 70 | 36 | 0.2 |

Due to the scientific characteristics of the ozone assimilation, 3-D chemistry products (D4FAPCHM, D4LAPCHM) will have a different set of pressure levels:

| Level | Pressure (hPa) | Level | Pressure (hPa) | Level | Pressure (hPa) |
| --- | --- | --- | --- | --- | --- |
| 1 | 1000 | 15 | 500 | 29 | 50 |
| 2 | 975 | 16 | 450 | 30 | 40 |
| 3 | 950 | 17 | 400 | 31 | 30 |
| 4 | 925 | 18 | 350 | 32 | 25 |
| 5 | 900 | 19 | 300 | 33 | 20 |
| 6 | 875 | 20 | 250 | 34 | 15 |
| 7 | 850 | 21 | 200 | 35 | 10 |
| 8 | 825 | 22 | 170 | 36 | 7 |
| 9 | 800 | 23 | 150 | 37 | 5 |
| 10 | 750 | 24 | 130 | 38 | 3 |
| 11 | 700 | 25 | 115 | 39 | 2 |
| 12 | 650 | 26 | 100 | 40 | 1 |
| 13 | 600 | 27 | 85 | 41 | 0.4 |
| 14 | 550 | 28 | 70 | 42 | 0.2 |

# Appendix D. Summary of differences between GEOS-3 and GEOS-4

In this section we summarize the differences between the GEOS-3 and GEOS-4 products.  We will not discuss the scientific characteristics of the systems, but only the differences in format and content of the products.  GEOS-3 products are generated using the GEOS-3 Data Assimilation System until October 1, 2002, after which products from the GEOS-4 Data Assimilation System will be produced.   The same 21 products are produced from both systems, 8 from First-look and 13 from Late-look.  The format of all products is the HDF-4 version of HDF-EOS.  Details of the differences follow.

- The horizontal resolution is different.  The GEOS-3 resolution is 360x181.  The GEOS-4 resolution is 288x181.

- The averaging periods of time-averaged products has been changed.  Averages are now between synoptic times rather than spanning them.  For example, the first average in a 3D 6-hourly file from GEOS-4 is the period from 00 GMT to 06 GMT.  The first average in a corresponding GEOS-3 file would be 21 GMT to 03 GMT.  This has changed the effective range times of the GEOS-4 time-averaged products.  See section 3 of this document for more information.

- The contents of most products changed.

  - tsyn2d_mis_x:

    - ALBEDO and TPW removed but still available as time-averaged in tavg2d_eng_x

    - VAVEU, VAVEV, and VAVET moved to tavg2d_eng_x, now time-averaged

    - SNOW removed but still available as time-averaged in tavg2d_lsm_x

    - GWET moved to tavg2d_eng_x as GWETTOP and GWETROOT, now time-averaged

    - TGROUND renamed to TSKIN

    - TROPQ added

  - tsyn3d_mis_p:

    - TKE removed

    - OMEGA moved to tavg3d_mom_p, now time-averaged

  - tavg2d_eng_x:

    - QICE, CT, VAVEQIAU, VAVEQFIL, and VAVETIAU removed

    - VAVEU, VAVEV, VAVET, GWETTOP, and GWETROOT added (formerly in tsyn2d_mis_x)

    - TGROUND renamed to TSKIN

    - PRECL added

    - PARDR and PARDF added (formerly in tavg2d_lsm_x)

  - tavg2d_str_x:

    - GWDUT, GWDVT, CU, and PIAU removed

    - Z0 split into Z0H and Z0M

    - PBL changed to PBLH (units changed from hPa to m)

  - tavg2d_lsm_x:

    - SNOWFALL, GREEN, and DLWDTC removed

    - PARDR and PARDF moved to tavg2d_eng_x

  - tavg2d_cld_x:

    - TAULOW, TAUMID, TAUHI, CLDTMP, and CLDPRS removed

  - tavg3d_cld_p:

    - CLDRAS removed

    - TAUCLD split into TAUCLI and TAUCLW

  - tavg3d_mom_p:

    - RFU, RFV, UIAU, VIAU, DUDT, and DVDT removed

    - OMEGA was added (formerly in tsyn3d_mis_p)

  - tavg3d_mst_p:

    - DQLS, QIAU, QFILL, and DQDT removed

  - tavg3d_tmp_p:

    - TURBT, MOISTT, DTLS, RADLW, RADSW, RFT, GWDT, TIAU, DTDT, LWCLR, and SWCLR removed

- Due to these changes, there are differences in the daily file sizes.

- The filename convention was changed slightly.  AM1 was changed to GEOS4.  The hour in the filename is different for time-averaged products due to the difference of time ranges mentioned above.  See section 5 for more details about the file naming convention.

- New ESDTs were defined for GEOS-4.  The names are listed in section 6 of this document.  For First-look the ESDT names now start with D4F and for Late-look D4L.  For GEOS-3 the names started with DFL and DLL.

The data contained in the tsyn2d_mis_x product is 3-hourly, however the source data from GOES-4 is 6-hourly.  The interim times are computed by time interpolating between synoptic times.  This is done to provide consistency with the corresponding GEOS-3 product.  See section 3 for more information.

# Appendix E: Additional products on eta vertical coordinates

A set of First-look (FLK) and Late-look (LLK) products defined on the GEOS-4 vertical coordinate grid (eta) will be produced starting in spring 2004.  Eta coordinates are generically known as atmosphere hybrid sigma pressure coordinates.  The two  eta-layer products will be daily files with four 6-hour time-averages for each variable.  These files are targeted for users involved in chemical transport work, but may be useful to a wider audience.  The tavg3d_mis_e  product is defined for 55 vertical layers, from the highest layer of the GCM (0.015 hPa) to the layer adjacent to the surface.   The  tavg3d_trp_e product  is defined for only the lowest 24 GCM eta layers because the variables included vanish above the tropopause. The time period for each six-hour average will be centered on one of the 4 synoptic times, i.e., 00 GMT will represent the average from 21 GMT to 03 GMT.  This is different than the pressure products, described in section 6,  which span the periods between synoptic times.  For more information, please see the diagram at the end of this appendix.

The GEOS-4 eta coordinate system can be described by the following equation:

p(i,j,k,t) = a(k) + b(k)*ps(i,j,t)

where for a given time t, p is the pressure at the coordinates i,j,k and a(k) and b(k) are components of the hybrid coordinate at the layer edge k.  To find the average p for a layer, one would average p at the edges k and k+1.  ps(i,j,t) is the surface pressure at the horizontal gridpoint (i,j) and time t.  a(k) and b(k) at 56 layer edges (25 edges for the 24 layer product) are stored as global metadata values in each eta product file.  They are also listed in a table near the end of this appendix.  For tavg3d_mis_e, when k=1, p = 1.0 Pa and when k=56, p=ps.  For tavg3d_trp_e, when k=1, p=3,381 Pa and when k=56, p=ps.

- tavg3d_mis_e (4 times per day)

FLK ECS short name: D4FAEMIS

FLK ECS long name: DAS First-look miscellaneous meteorology fields, time-averaged on eta coordinates

LLK ECS short name: D4LAEMIS

LLK ECS long name: DAS Late-look miscellaneous meteorology fields, time-averaged on eta coordinates

Size: 551 MB/day

Dimensions:

longitude: 288

latitude: 181

vertical layers (eta): 55

| Variable Name | Description | Units |
| --- | --- | --- |
| PS* | Surface pressure (two-dimensional field) | Pa |
| DIABDT | T Tendency - Total diabatic (physics) | K/s |
| HGHT | Geopotential height at mid-layer | m |
| HGHTE | Geopotential height at layer top | m |
| KH | Vertical diffusion diffusivities (heat/moisture) | m2/s |
| KM | Eddy diffusivity for momentum | m2/s |
| OMEGA | Vertical pressure velocity | Pa/s |
| PV | Ertels potential vorticity | K*m2/(kg*sec) |
| RH | Relative humidity after cloud physics | percent |
| SPHU* | Specific humidity | kg/kg |
| TMPU | Temperature | K |
| UWND | U wind | m/s |
| VWND | V wind | m/s |

- tavg3d_trp_e (4 times per day)

FLK ECS short name: D4FAETRP

FLK ECS long name: DAS First-look transport fields, time-averaged on  eta coordinates

LLK ECS short name: D4LAETRP

LLK ECS long name: DAS Late-look transport fields, time-averaged on eta coordinates

Size: 382 MB/day

Dimensions:

longitude: 288

latitude: 181

vertical layers (eta): 24

| Variable Name | Description | Units |
| --- | --- | --- |
| PS* | Surface pressure (two-dimensional field) | Pa |
| CLDTOT | 3-D Cloud fraction | fraction |
| CMFDQR2 | Rain production rate - Hack convection | kg/kg/s |
| CMFDTR | Detrainment mass flux - Hack convection | Pa/s |
| CMFETR | Entrainment mass flux - Hack convection | Pa/s |
| CMFMC | Total moist convection mass flux | Pa/s |
| CMFMC2 | Hack moist convection mass flux | Pa/s |
| DQRL | Rain production rate - large-scale | kg/kg/s |
| DTRAIN* | Detrainment cloud mass flux (Ave) | Pa/s |
| HKBETA | Overshoot parameter in Hack scheme | fraction |
| HKETA | Mass flux without overshoot in Hack scheme | kg/m2/s |
| MOISTQ | Q tendency - moist physics | kg/kg/s |
| TAUCLI | Cloud optical depth ice | non-dimensional |
| TAUCLW | Cloud optical depth water | non-dimensional |
| ZMDQR | Rain production rate - Z&M convection | kg/kg/s |
| ZMDU | Updraft detrainment mass flux - Z&M convection | Pa/s |
| ZMED | Downdraft entrainment mass flux - Z&M convection | Pa/s |
| ZMEU | Updraft entrainment mass flux - Z&M convection | Pa/s |
| ZMMD | Downdraft mass flux - Z&M convection (Ave) | Pa/s |
| ZMMU | Updraft mass flux - Z&M convection | Pa/s |

*- These variables are also available in other GEOS-4 surface or pressure products, but in the eta products we use standard SI units or derivations.  In particular, tendency terms in pressure level products are expressed as rates of change per day, while the eta products are per second.  Moisture concentrations are expressed here as kg/kg, while the pressure products use g/kg. Surface pressure is expressed in Pa instead of hPa.   Mass flux terms are expressed as Pa/s.

Filenames of the eta products conform to the conventions described in section 5 of this document.  The beginning and ending times will be slightly different than for the pressure products due to the differences in the time-averaging period.  Here is an example of filenames from First-look.

DAS.flk.asm.tavg3d_mis_e.GEOS403.2003070121.2003070221.V01

DAS.flk.asm.tavg3d_trp_e.GEOS403.2003070121.2003070221.V01

The following table contains ak and bk pairs for each layer edge k.  There are 56 layer edges that  define 55 layers.  Note that for the 24 layer tavg3d_trp_e  product, there are 25 layer edges and the k values are denoted with ( )s.  These arrays can be found as floating point global metadata attributes in each eta product file.

| k | ak | bk |  | k | ak | bk |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 1.000 | 0.000 |  | 29 | 1979.155 | 0.000 |
| 2 | 2.000 | 0.000 |  | 30 | 2373.036 | 0.000 |
| 3 | 3.270 | 0.000 |  | 31 | 2836.782 | 0.000 |
| 4 | 4.759 | 0.000 |  | 32 (1) | 3380.996 | 0.000 |
| 5 | 6.600 | 0.000 |  | 33 (2) | 4017.542 | 0.000 |
| 6 | 8.934 | 0.000 |  | 34 (3) | 4764.393 | 0.000 |
| 7 | 11.970 | 0.000 |  | 35 (4) | 5638.794 | 0.000 |
| 8 | 15.950 | 0.000 |  | 36 (5) | 6660.338 | 0.000 |
| 9 | 21.135 | 0.000 |  | 37 (6) | 7851.230 | 0.000 |
| 10 | 27.853 | 0.000 |  | 38 (7) | 9236.566 | 0.000 |
| 11 | 36.504 | 0.000 |  | 39 (8) | 10866.343 | 0.000 |
| 12 | 47.581 | 0.000 |  | 40 (9) | 12783.700 | 0.000 |
| 13 | 61.678 | 0.000 |  | 41 (10) | 15039.300 | 0.000 |
| 14 | 79.513 | 0.000 |  | 42 (11) | 17693.000 | 0.000 |
| 15 | 101.944 | 0.000 |  | 43 (12) | 20119.209 | 0.007 |
| 16 | 130.051 | 0.000 |  | 44 (13) | 21686.492 | 0.028 |
| 17 | 165.079 | 0.000 |  | 45 (14) | 22436.287 | 0.064 |
| 18 | 208.497 | 0.000 |  | 46 (15) | 22388.469 | 0.115 |
| 19 | 262.021 | 0.000 |  | 47 (16) | 21541.752 | 0.183 |
| 20 | 327.643 | 0.000 |  | 48 (17) | 19873.783 | 0.270 |
| 21 | 407.657 | 0.000 |  | 49 (18) | 17340.318 | 0.378 |
| 22 | 504.680 | 0.000 |  | 50 (19) | 13874.440 | 0.510 |
| 23 | 621.680 | 0.000 |  | 51 (20) | 10167.165 | 0.643 |
| 24 | 761.984 | 0.000 |  | 52 (21) | 6609.843 | 0.765 |
| 25 | 929.294 | 0.000 |  | 53 (22) | 3546.596 | 0.868 |
| 26 | 1127.689 | 0.000 |  | 54 (23) | 1270.494 | 0.943 |
| 27 | 1364.339 | 0.000 |  | 55 (24) | 0.000 | 0.985 |
| 28 | 1645.707 | 0.000 |  | 56 (25) | 0.000 | 1.000 |

Figure 1 - This is a graphical representation of the averaging periods for GEOS-4 3D time-averaged products.  Note that eta-layer products are centered on synoptic times while pressure-level products span the range between synoptic times.

# REFERENCES

GMAO Operations web page: http://gmao.gsfc.nasa.gov/Operations/

DAO, 2002: Algorithm Theoretical Basis Document, Data Assimilation Office,

NASA's Goddard Space Flight Center.

Dopplick, T., 1997: The Role of Metadata in EOSDIS (DRAFT). EOSDIS Technical

Paper 160-TP-013-001.

Gross, C., 1997: B.0 Earth Science Data Model for the ECS Project. EOSDIS

Technical Paper 420-TP-015-001.

NOAA, 1995: Conventions for the Standardization of NetCDF Files (COARDS). http://ferret.wrc.noaa.gov/noaa_coop/coop_cdf_profile.html

NCSA, 1999: The NCSA HDF Home Page. http://hdf.ncsa.uiuc.edu/

NASA, 1999: HDF-EOS Standards. http://hdfeos.gsfc.nasa.gov/

deWitt, Shaun, 1996: Writing HDF-EOS Grid Products for Optimum Subsetting Services. ECS Technical Paper 170-TP-007-001.